## Slide 1: Lecture 1: Introduction
Go over the syllabus/schedule
We will cover chapters 1-7 of Shultis and Faw AND learn MCNP (source and detector)
  We will also use MCNP for many homework assignments, from simple to complex problems
MCNP is available from RSICC
  The early MCNP homework will not be late until the first test
  BUT the tests will include MCNP input

## Slide 2: Contact RSICC soon
Go to http://www-rsicc.ornl.gov/
Customer Service
Registration/Requests
  New User
      Organization type: University
      Project type: Radiation dam. or Other
      Funding source #1: US University
      Funding %:100
      Customer feedback: I am a NE student at UT and need MCNP for NE406 Radiation Protection and Shielding course
Get MCNP6.1/MCNP5/MCNPX (C00810 MNYCP 00) or the next one (…-EXE)

## Slide 3
Course overview

## Slide 4: Course content
Radiation transport problems not covered by reactor analysis and criticality safety
I am a practical guy teaching a practical course:
  Just-in-time physics discussion before expanding your MCNP capabilities
From book:
  How radiation is created
  How it migrates from its source
  How it interacts with matter
  How to calculate the “effects of interest”

## Slide 5: Course content (2)
From MCNP:
  How shielding is really done
Practical situations we will cover
  Shield design
  Isotope production
  Medical applications
  Industrial uses of radiation (including food irradiation)

## Slide 6: Course content (3)
Role of computers vs. Hand calculations
  Hand calculations
    Simplified geometry (usually line-of-sight, single material)
    Simplified energy treatment
  Computer calculation
    Detailed geometry and energy treatment
    Solve Boltzmann Transport Equation (BTE)
    Detailed data required: Source of much error > 20 MeV
    Expensive, time-consuming (analyst and computer)

## Slide 7
Monte Carlo overview

## Slide 8: General Overview of MC
Monte Carlo: Stochastic approach
  Statistical simulation of individual particle histories
  Keep score of quantities you care about
  Most of mathematically interesting features come from “variance reduction methods” in which we modify the particle history (in a fair way) to be more efficient
  Gives results PLUS standard deviation = statistical measure of how reliable the answer is

## Slide 9: Mathematical basis
Statistical simulation driven by random number generator: 0<x<1, with a uniform distribution.
These random numbers are translated (using methods learned in NE582) into physical “decisions” that nature makes while a particle is moving around
“Score-keeping” is done on items of interest (to the analyst) using the simple statistical formula:

## Slide 10: Simple Walkthrough
Six types of decisions to be made:
  Where the particle is born
  Initial particle energy
  Initial particle direction
  Distance to next collision
  Type of collision
  Outcome of scattering collision (E, direction)
Also, somewhere along the way, physical parameters you are interested in (tallies) are contributed to

## Slide 11: Chapters of the text
Introduction
Characterization of Radiation Fields and Sources
Interaction of Radiation with Matter
Common Radiation Sources Encountered in Shield Design
Photon and Neutron Response Functions
Basic Methods for Radiation Dose Calculations
Special Techniques for Photons
Special Techniques for Neutrons
Special Techniques for Charged Particles
Deterministic Transport Theory
Monte Carlo Methods for Radiation Transport Calculations

## Slide 12: Who is this?
2012-6465
247-843
912-327
54-75212
0-20
740184-75390
42-98
1251-1439
34-74
646-62712

## Slide 13
Simple MCNP Examples

## Slide 14: Sections of MCNP Input
Sections of input
  Title (1 line)
  Cell cards—A cell is a 3D region containing a single material
  Surface cards—A surface is a 2D plane, sphere, cylinder, cone, etc., that bounds one or more cells
  Data cards: Everything else—materials, sources, tallies, variance reduction parameters, number of histories, etc.
  A SINGLE blank line must follow Sections 2 and 3 (and NO OTHER blank lines are allowed)

## Slide 15: Case 1: Empty sphere
Simple point source in void; Tally = surface crossing
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 0 -1 imp:p=1
999 0 1 imp:p=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 7
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode p
sdef par 2 pos 0 0 0 erg 2
f1:p 1

## Slide 16: Comments
You may enter comments (messages to yourself) in the deck by either:
  Beginning a line with the letter “c” (upper or lower case) FOLLOWED BY A BLANK:
  This is the title
  c This is a comment
  Entering “$” anywhere on a line and following with your comment
  m1 1001 2 8016 1 $ This is water

## Slide 17: Case 1: Empty sphere
Simple point source in void; Tally = surface crossing
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 0 -1 imp:p=1
999 0 1 imp:p=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 7
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode p
sdef par 2 pos 0 0 0 erg 2
f1:p 1

## Slide 18: Continuing lines
MCNP only reads out to 80 columns of input. If you have more than that to enter (or just to make it look neater), you may CONTINUE on the next line as long as you either:
  End a line with “&” plus at least one blank:
  m1 1001 2 &
  8016 1
  Leaving the first 5 columns blank on continuation lines:
  m1 1001 2
  8016 1
(Be careful not to start with >4 blanks if you DON’T want to continue a line)

## Slide 19: Surface Description
Surfaces comprise:
  Mnemonic keyword (px,py,pz,cz,so,rpp,sph)
  Parameters (e.g.,radius of sphere)
  “Sense”=negative or positive “side” of the surface
Most common are planes, cylinders, spheres
  PX, PY, PZ: negative direction is negative sense
  CX, CY, CZ: inside is negative, outside positive
  S, SO, SX, SY, SZ: inside negative, outside positive
  “macrobodies”: inside negative, outside positive

## Slide 22: Macro Spheres: SPH
Syntax:
Description: General sphere, centered on with radius R

## Slide 23: Case 1: Empty sphere
Simple point source in void; Tally = surface crossing
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 0 -1 imp:p=1
999 0 1 imp:p=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 7
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode p
sdef par 2 pos 0 0 0 erg 2
f1:p 1

## Slide 24: Cell Description
Cell cards contain:
  Material number and density: (void uses ONE 0 entry)
    Positive densityatoms/bn/cm
    Negative densityg/cc
  Boolean combinations of the surfaces
    Blanks between surfaces=intersection (AND)
      “1 -2”  intersection of positive side of surface 1 and negative side of surface 2
    Colons=union (OR)
      “1:-2”union of positive side of surface 1 and negative side of surface 2
    Parentheses creates priority groupings
      “(1 -2):(3 -4)inside of parentheses evaluated before the union
    #=complement operator (NOT)
      “#1” outside of CELL 1
      “#(2 -3 )” complement of intersection of positive side of SURFACE 2 and negative side of SURFACE 3

## Slide 25: Case 1: Empty sphere
Simple point source in void; Tally = surface crossing
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 0 -1 imp:p=1
999 0 1 imp:p=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 7
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode p
sdef par 2 pos 0 0 0 erg 2
f1:p 1

## Slide 26: Cell importances: IMP
Syntax:
Description: Sets cell importance=Expected relative contribution of a particle of type n introduced into a cell
This can either be a separate entry in the DATA section
OR
can be entered as part of each individual CELL card.

## Slide 27: Case 1: Empty sphere
Simple point source in void; Tally = surface crossing
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 0 -1 imp:p=1
999 0 1 imp:p=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 7
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode p
sdef par 2 pos 0 0 0 erg 2
f1:p 1

## Slide 28: Case 1: Empty sphere
Simple point source in void; Tally = surface crossing
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 0 -1
999 0 1
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 7
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode p
sdef par 2 pos 0 0 0 erg 2
f1:p 1
imp:p 1 0

## Slide 29: Particles to follow: MODE
Syntax: MODE n/p/e
Description: Picks the particle types to be tracked
n = neutrons
p = photons
e = electrons
h = protons
etc.

## Slide 30: Case 1: Empty sphere
Simple point source in void; Tally = surface crossing
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 0 -1 imp:p=1
999 0 1 imp:p=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 7
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode p
sdef par 2 pos 0 0 0 erg 2
f1:p 1

## Slide 31: Source Definition: SDEF Card
SDEF card
For a point source:
  PAR=1/2/3 particle type (1/2/3=n/p/e)
  ERG=xx Energy of particle (MeV)
  POS=x y z Position indicator
Example: 9.5 MeV neutron source at point (1., 4., 5.)
SDEF PAR=1 ERG=9.5 POS=1 4 5

## Slide 32: Case 1: Empty sphere
Simple point source in void; Tally = surface crossing
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 0 -1 imp:p=1
999 0 1 imp:p=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 7
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode p
sdef par 2 pos 0 0 0 erg 2
f1:p 1

## Slide 33: Simple Tallies
Tallies
  Tally names begin with F followed by a integer
  :n :p :e denotes particle to watch
  Tally type is units units digit of integer
    F541:n is surface crossing of neutrons
    F12:p is surface flux of photons
    F344:e is cell flux of electrons
    F15:p is point flux of photons
  In input card cell and surface/cell/point values follow name (parentheses combine surfaces/cells into a single tally)

## Slide 34: Case 1: Empty sphere
Simple point source in void; Tally = surface crossing
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 0 -1 imp:p=1
999 0 1 imp:p=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 7
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode p
sdef par 2 pos 0 0 0 erg 2
f1:p 1

## Slide 35: Running MCNP
Input is created in a text file with a particular required format
MCNP is executed from the command line prompt:
  C>mcnp6  Input must be in inp; output will be in outp
  C>mcnp6 inp=infile outp=outfile
  C>mcnp6 name=filename  Output will be in filenameo
Special tricks to know:
  mcnp6.exe must be in your PATH (This is automatic if you installed the RSICC DVD).
  The MCNP_DATA must have been installed
  MCNP will not overwrite a file that exists with the same name—it will just fail.
  So, you have to eliminate previous output files (there are several of these)

## Slide 36: Stopping MCNP
Three ways to stop an MCNP case
  From input deck:
    NPS xx Number of histories to run
    CTME xx Number of minutes to run
    BothIt will stop when the first of the two are satisfied
  From console:
    MCNP can be stopped from the console with “Control-C”, then “q” (gracefully)

## Slide 37: Case 1: Empty sphere
Simple point source in void; Tally = surface crossing
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 0 -1 imp:p=1
999 0 1 imp:p=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 7
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode p
sdef par 2 pos 0 0 0 erg 2
f1:p 1
nps 10000

## Slide 38: Where is my answer?
Throughout the course, we will be examining the extensive MCNP6 output
For now, though, let’s just find the answer by:
  Opening the output deck.
    It will either be named what you TOLD it to name it OR MCNP will automatically add the letter “o” to the end of your input deck.
  Search on “tally” in the deck

## Slide 39: Tally output
.
.
.
tally 1 nps = 10000
tally type 1 number of particles crossing a surface.
tally for photons
surface 1
1.00000E+00 0.0000
.
.
.
On the last line:
  The first number is the answer in units (for F1) of “surface crossings per source particle:
    The answer is 1.000 because all source particles reach cross the sphere surface on the way out (and never return)
  The second number is the fractional standard deviation (actually statisticians call it the “fractional standard error” since it is an approximation).
    In our case it is 0.000 because all 10000 histories scored exactly the same answer

## Slide 40: Material Description: Mm Card
Materials are described by (isotope,density) pairs
  Isotope—specified by ZZAAA
    1001H-1
    8016O-16
    92235 U-235
  If AAA is 000, specifies the natural isotopic mix for an element
    82000natural lead
    8000natural oxygen
  Density—Relative number (+) or mass (-) for each isotope
Example: Water
M1 1001 2 8016 1
OR
M2 1001 -1.998335 8016 -15.8575

## Slide 41: Case 2: Lead sphere
Simple point source in lead ; Tally = surface crossing
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 1 -11.35 -1 imp:p=1
999 0 1 imp:p=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 7
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode p
sdef par 2 pos 0 0 0 erg 2
m1 82000 1
f1:p 1
nps 10000 Result: 0.0845 +/- 3.31%