## Slide 1: Lecture 3: K-effective
Material specification
K-effective calculations
Beam sources
Collecting particles by energy
Collection particle by direction

## Slide 2: Photon coefficients

## Slide 3: Material Description: Mm Card
Materials are described by (isotope,density) pairs
  Isotope—specified by ZZAAA
    1001H-1
    8016O-16
    92235 U-235
  If AAA is 000, specifies the natural isotopic mix for an element
    82000natural lead
    8000natural oxygen
  Density—Relative number (+) or mass (-) for each isotope
Example: Water
M1 1001 2 8016 1
OR
M2 1001 -1.998335 8016 -15.8575

## Slide 4: Case 1: Lead sphere
Simple point source in lead ; Tally = surface crossing
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 1 -11.35 -1 imp:p=1
999 0 1 imp:p=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 7
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode p
sdef par 2 pos 0 0 0 erg 2
m1 82000 1
f1:p 1
nps 10000 Result: 0.0815 +/- 3.39%

## Slide 5: Criticality card: KCODE
Syntax:
Description: Criticality equivalent of SDEF card. Sets up number of cycles, number of histories per cycle, number of cycles to skip, etc.
NSRCK=#histories per cycle
RKK=initial keff guess
IKZ=#cycles to skip
KCT=#cycles to be done
MCNP5 Manual Page: 3-75

## Slide 6: Initial source card: KSRC
Syntax:
Description: Source locations for initial cycle of criticality calculations. [You can ALSO use the regular SDEF card.]
MCNP5 Manual Page: 3-76

## Slide 7: Case 2: Uranium 235
Spherical U-235 k-eff
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 1 -18.81 -1 imp:n=1
999 0 1 imp:n=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 7
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode n
kcode 100 1.0 0 100
ksrc 0 0 0
m1 92235 1 Result: k-eff = 0.85546 +/- 0.00628

## Slide 8: HW 3.1
Use MCNP to find the critical radius of a solid sphere of uranium 235
Repeat with one inch of water outside the uranium
(Consider k-effective of 0.995-1.005 to be critical. Run both to at least FSD=0.001)

## Slide 9: Beam sources
  SDEF variables used:
  POS=Position of the source center
  VEC=Vector of direction of the beam
  DIR=Direction cosine vs. VEC
  Example: 1.5 MeV beam of neutrons travelling up from point (1,2,3):
  SDEF par 1 erg 1.5 pos 1 2 3 vec 0 0 1 dir 1

## Slide 10: Case 3: Sigma-total calc
Photon total cross section in water
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 1 -1 -1 imp:p=1
2 0 1 -2 imp:p=1
999 0 2 imp:p=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 rcc 0 0 0 1 0 0 .0001
2 sph 0 0 0 100
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode p
sdef par=2 erg=1 dir=1. vec=1 0 0 pos=-1 0 0
f1:p 1.1 1.2 1.3
m1 1001 2 8016 1

## Slide 11: HW 3.2
Use MCNP with a beam source and a small cylindrical sample to estimate the mass attenuation coefficient (mu/rho) for a 10 MeV photon impinging on lead +/- 0.0001 cm2/g
Repeat for 1 MeV and 100 keV