## Slide 1: Source Definition: SDEF Card

## Slide 3: Source Definition: SDEF Card
SDEF card
For a point source:
  PAR=1/2/3 particle type (1/2/3=n/p/e)
  ERG=xx Energy of particle (MeV)
  POS=x y z Position indicator
Example: 9.5 MeV neutron source at point (1., 4., 5.)
SDEF PAR=1 ERG=9.5 POS=1 4 5

## Slide 4: Advanced Source Specification
  Source distributions
  Volumetric sources
  Surface sources
  Energy-dependent binning

## Slide 5: X axis of a distribution: SI
Syntax:
Description: The SIn and SPn cards work together to define a pdf to select a variable from.
option= blank or Hhistogram
=Ldiscrete
=A(x,y) pairs interpolated
=Sother distribution #’s
MCNP5 Manual Page: 3-61

## Slide 6: Y axis of a distribution: SP
Syntax:
Description: Specification of y axis of pdf for distribution n.
option=blankcompletes SI
=-ppredefined function
The P values are the y-axis values OR the parameters for the desired function p—and the SI numbers are the lower and upper limits. (Table 3.4)
MCNP5 Manual Page: 3-61

## Slide 7: Examples
SI2 H 0 5 20
SP2 0 1 2
…
SI3 L 1 2
SP3 1 2
…
SI4 A 0 5 20
SP4 0 1 2
…
SI5 1 5
SP5 –21 2

## Slide 8: Input shortcuts
Description: Saving keystrokes
MCNP5 Manual Page: 3-4
Syntax:
  2 4R => 2 2 2 2 2
  1.5 2I 3 => 1.5 2.0 2.5 3.0
  0.01 2ILOG 10 => 0.01 0.1 1 10
  1 1 2M 3M 4M => 1 1 2 6 24
  1 3J 5.4 => 1 d d d 5.4
    (where d is the default value for that entry)

## Slide 9: Source description variables
Commands:
  POS=Position of a point of interest
  RAD=How to choose radial point
  AXS=Direction vector of an axis
  EXT=How to choose point along a vector
  X,Y,Z=How to choose (x,y,z) dimensions
  VEC=Vector of interest
  DIR=Direction cosine vs. VEC vector
Combinations:
  X,Y,Z: Cartesian (cuboid) shape
  POS, RAD: Spherical shape
  POS, RAD, AXS, EXT: Cylindrical shape
  VEC,DIR: Direction of particle

## Slide 10: X,Y,Z: Cartesian (cuboid) shape
Rectangular source
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 0 -1 imp:n=1
999 0 1 imp:n=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 20
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode n
sdef x d1 y d2 z d3
si1 h -5 5
sp1 0 1
si2 h -5 5
sp2 0 1
si3 h -5 5
sp3 0 1

## Slide 11: POS, RAD: Spherical shape
Spherical source
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 0 -1 imp:n=1
999 0 1 imp:n=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 20
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode n
sdef pos 0 0 0 rad d1
si1 0 5
sp1 -21 2

## Slide 12: POS, RAD, AXS, EXT: Cylindrical shape
Cylindrical source
c *********************************************************************
c *
c Cells *
c *
c *********************************************************************
1 0 -1 imp:n=1
999 0 1 imp:n=0
c *********************************************************************
c *
c Surfaces *
c *
c *********************************************************************
1 sph 0 0 0 20
c *********************************************************************
c *
c Data cards *
c *
c *********************************************************************
mode n
sdef pos 0 0 0 ext d1 axs 0 0 1 rad d2
si1 -5 5
sp1 0 1
si2 0 5
sp2 -21 1

## Slide 13: Appendix H

## Slide 14: HW 4.1
Use the Appendix H data to give me the appropriate MCNP source description for an isotropic 1 microCurie Co-60 point source that is 10 years old.
Use a hand calculation to find the total flux at a distance of 100 cm
Check your flux calculation with an MCNP calculation using an F2 tally

## Slide 15: HW 4.2
Use an MCNP calculation of a beam impinging on the small water sample to estimate the total cross section of water for 0.1 MeV, 1 MeV, and 10 MeV photons. Compare your answers to the values in Appendix C of the text.

## Slide 16: HW 4.3
If you have a parallelepiped volumetric isotropic source with a strength of 100 particles/cc/sec and W=20 cm (x dimension), L=10 cm (y dimension), H=50 cm (z dimension):
Find the equivalent surface source if the analyst judges that L is insignificant.
Find the equivalent line source if the analyst judges that W is also insignificant; and
Find the equivalent point source if the analyst judges that H is insignificant as well.
For each of these be sure the source size, placement and strength (in appropriate units) is specified.

## Slide 17: HW 4.3 (cont’d)
Use MCNP to model each of the sources (3D, 2D, 1D, point) and compare the total flux centered a distance of 250 cm away from the W-H plane. Use an F5 tally.