## Slide 1: Lesson 4: Computer method overview
Neutron transport overview
  Comparison of deterministic vs. Monte Carlo
User-level knowledge of Monte Carlo
Advantages and disadvantages of each

## Slide 2: Neutron balance equation
Scalar flux/current balance
Used in shielding, reactor theory, crit. safety, kinetics

## Slide 3: Neutron transport
Scalar vs. angular flux
Boltzmann transport equation
  Neutron accounting balance
  General terms of a balance in energy, angle, space
Deterministic
  Subdivide energy, angle, space and solve equation
  Get k-effective and flux
Monte Carlo
  Numerical simulation of transport
  Get particular flux-related answers, not flux everywhere

## Slide 4: Deterministic solution
Subdivide everything:
  Energy: Multigroup
  Space: Chop up space into “mesh cells”
  Angle: Only allow particles to travel in particular directions
Use balance condition to figure out (and save) the flux as a function of space, energy, direction
Spatial and angular flux for Group 1 (10 MeV-20 MeV)
Source

## Slide 5: Statistical solution (“simulation”)
Continuous in Energy, Space, Angle
Sample (poll) by following “typical” neutrons
  Drop a million neutrons into the system and see how many new neutrons are created: ratio is k-effective
Particle track of two 10 MeV fission neutrons
Fissile
Absorbed
Fission

## Slide 6: General Overview of MC
Monte Carlo: Stochastic approach
  Statistical simulation of individual particle histories
  Keep score of quantities you care about (for us MOSTLY k-effective, but we also want to know where fission is occurring)
  Gives results PLUS standard deviation = statistical measure of how reliable the answer is

## Slide 7: Special input variables user must provide
Must deal w/ “generations”=outer iteration
  Fix a fission source spatial shape
  Find new fission source shape and eigenvalue
User must specify # of generations AND # of histories per generation AND # of generation to “skip”
Skipped generations allow the original lousy spatial fission distribution to improve before we really start keeping “score”
KENO defaults: 203 generations of 1000 histories per generation, skipping first 3

## Slide 8: Advantages and disadvantages of each
 | Advantages | Disadvantages
Discrete Ordinates (deterministic) | Fast (1D, 2D) Accurate for simple geometries Delivers answer everywhere: = Complete spatial, energy, angular map of the flux 1/N (or better) error convergence | Slow (3D) Multigroup energy required Geometry must be approximated Large computer memory requirements User must determine accuracy by repeated calculations
Monte Carlo (stochastic) | “Exact” geometry Continuous energy possible Estimate of accuracy given | Slow (1,2,3D) Large computer time requirements 1/N1/2 error convergence