## Slide 1: Lesson 6: Experments, etc.
SCALE examples w/ parametric studies
Overview of the “benchmark book”

## Slide 2
SCALE Sequence CSAS1

## Slide 3: SCALE overview
Standard Computerized Analysis for Licensing Evaluation (I think)
Pulls together what used to be separate nuclear analysis codes into a single input package
  Saves duplication of problem description
  Allows for reduced user control: Makes it easier for reviewers
  Makes “black box” use much more likely
Organized in “sequences: CSAS1X & CSAS25 in this course
  Resonance processing (BONAMI & NITAWL)
  Transport calculation (XSDRNPM or KENO-Va)

## Slide 4: SCALE input: Material descriptions
Several ways to specify materials
  Pre-mixed mixtures
  Natural elements (with modification allowed)
  By isotope (be careful with densities)
Can have several lines to define a single material--Use VF to mix
Example of using the manual description

## Slide 5: Sample CSAS1X input
=csas1 parm=(nitawl)
fig. 2-2, point 1
44groupndf5
read composition
pu 1 1 293 94239 100 end
h2o 2 1 293 end
end composition
read celldata
multiregion spherical left_bdy=reflected right_bdy=vacuum
cellmix=500 end
1 5
end zone
end celldata
end

## Slide 6: CSAS1X output
PRIMARY MODULE ACCESS AND INPUT RECORD ( SCALE DRIVER - 95/03/29 - 09:06:37 )
MODULE CSAS1X WILL BE CALLED
HW PROBLEM #1
27GROUPNDF4 MULTIREGION
URANIUM 1 0.985 293 92234 1 92235 93.2 92236 .2 92238 5.6 END
END COMP
SPHERICAL VACUUM REFLECTED 0 END
1 8.72 END ZONE
SECONDARY MODULE O0O008 HAS BEEN CALLED.
MODULE O0O008 IS FINISHED. COMPLETION CODE 0. CPU TIME USED 0.88 (SECONDS).
SECONDARY MODULE O0O002 HAS BEEN CALLED.
MODULE O0O002 IS FINISHED. COMPLETION CODE 0. CPU TIME USED 23.01 (SECONDS).
SECONDARY MODULE O0O001 HAS BEEN CALLED.
MODULE O0O001 IS FINISHED. COMPLETION CODE 0. CPU TIME USED 32.30 (SECONDS).
MODULE CSAS1X IS FINISHED. COMPLETION CODE 0. CPU TIME USED 58.77 (SECONDS).
Part 1: Repeat of input file

## Slide 7: CSAS1X output, cont’d
BBBBBBBBBBBB OOOOOOOOOOO NN NN AAAAAAAAA MM MM IIIIIIIIIIII 22222222222
BBBBBBBBBBBBB OOOOOOOOOOOOO NNN NN AAAAAAAAAAA MMM MMM IIIIIIIIIIII 2222222222222
BB BB OO OO NNNN NN AA AA MMMM MMMM II 22 22
BB BB OO OO NN NN NN AA AA MM MM MM MM II 22
BB BB OO OO NN NN NN AA AA MM MM MM MM II 22
BBBBBBBBBBBB OO OO NN NN NN ------------- AAAAAAAAAAAAA MM MMM MM II 22
BBBBBBBBBBBB OO OO NN NN NN ------------- AAAAAAAAAAAAA MM M MM II 22
BB BB OO OO NN NN NN AA AA MM MM II 22
BB BB OO OO NN NN NN AA AA MM MM II 22
BB BB OO OO NN NNNN AA AA MM MM II 22
BBBBBBBBBBBBB OOOOOOOOOOOOO NN NNN AA AA MM MM IIIIIIIIIIII 2222222222222
BBBBBBBBBBB OOOOOOOOOOO NN NN AA AA MM MM IIIIIIIIIIII 2222222222222
SSSSSSSSSSS CCCCCCCCCCC AAAAAAAAA LL EEEEEEEEEEEEE PPPPPPPPPPPP CCCCCCCCCCC
SSSSSSSSSSSSS CCCCCCCCCCCCC AAAAAAAAAAA LL EEEEEEEEEEEEE PPPPPPPPPPPPP CCCCCCCCCCCCC
SS SS CC CC AA AA LL EE PP PP CC CC
SS CC AA AA LL EE PP PP CC
SS CC AA AA LL EE PP PP CC
SSSSSSSSSSSS CC AAAAAAAAAAAAA LL EEEEEEEEE ------------- PPPPPPPPPPPPP CC
SSSSSSSSSSSS CC AAAAAAAAAAAAA LL EEEEEEEEE ------------- PPPPPPPPPPPP CC
SS CC AA AA LL EE PP CC
SS CC AA AA LL EE PP CC
SS SS CC CC AA AA LL EE PP CC CC
SSSSSSSSSSSSS CCCCCCCCCCCCC AA AA LLLLLLLLLLLLL EEEEEEEEEEEEE PP CCCCCCCCCCCCC
SSSSSSSSSSS CCCCCCCCCCC AA AA LLLLLLLLLLLLL EEEEEEEEEEEEE PP CCCCCCCCCCC
0000000 99999999999 // 22222222222 44 // 99999999999 7777777777777
000000000 9999999999999 // 2222222222222 444 // 9999999999999 777777777777
00 00 99 99 // 22 22 4444 // 99 99 77 77
00 00 99 99 // 22 44 44 // 99 99 77
Part 2: BONAMI output: Check input

## Slide 8: CSAS1X output, cont’d
P R O B L E M D E S C R I P T I O N
IGR--GEOMETRY (0/1/2/3--INF MED/SLAB/CYL/SPHERE 3
IZM--NUMBER OF ZONES OR MATERIAL REGIONS 1
MS--MIXING TABLE LENGTH 4
IBL--SHIELDED CROSS SECTION EDIT OPTION (0/1--NO/YES) 0
IBR--BONDARENKO FACTOR EDIT OPTION (0/1--NO/YES) 0
ISSOPT--DANCOFF FACTOR OPTION 0
CONVERGENCE CRITERION 1.00000E-03
GEOMETRY CORRECTION FACTOR FOR WIGNER RATIONAL APPROXIMATION 1.350E+00
…
M I X I N G T A B L E
ENTRY MIXTURE ISOTOPE NUMBER DENSITY NEW IDENTIFIER
1 1 92234 4.82827E-04 1092234
2 1 92235 4.48073E-02 1092235
3 1 92236 9.57449E-05 1092236
4 1 92238 2.65827E-03 1092238
GEOMETRY AND MATERIAL DESCRIPTION
ZONE MIXTURE OUTER DIMENSION TEMPERATURE EXTRA XS TYPE (0/1--FUEL/MOD)
1 1 8.72000E+00 2.93000E+02 9.08249E-02 0
1787 LOCATIONS OF 100000 AVAILABLE ARE REQUIRED TO MAKE A NEW MASTER CONTAINING THE SELF-SHIELDED VALUES
NO NUCLIDES IN YOUR PROBLEM HAVE BONDARENKO FACTOR DATA**BONAMI WILL COPY FROM LOGICAL 11 TO LOGICAL 1
BONAMI input, cont’d

## Slide 9: CSAS1X output, cont’d
NUCLIDES FROM XSDRN TAPE
1 URANIUM-234 ENDF/B-IV MAT 1043 UPDATED 08/12/94 1092234
2 URANIUM-235 ENDF/B-IV MAT 1261 UPDATED 08/12/94 1092235
3 U-236 1163 SIGO=5+4 NEWXLACS P-3 293K F-1/E-M(1.+5) UPDATED 08/12/94 1092236
4 URANIUM-238 ENDF/B-IV MAT 1262 UPDATED 08/12/94 1092238
URANIUM-234 ENDF/B-IV MAT 1043 UPDATED 08/12/94 1092234 TEMPERATURE= 293.00
RESONANCE DATA FOR THIS NUCLIDE
MASS NUMBER (A) = 232.029 TEMPERATURE(KELVIN) = 293.000
POTENTIAL SCATTER SIGMA = 10.021 LUMPED NUCLEAR DENSITY = 4.8282678E-04
SPIN FACTOR (G) = 6948.450 LUMP DIMENSION (A-BAR) = 8.7200003E+00
INNER RADIUS = 0.0000000E+00 DANCOFF CORRECTION (C) = 0.0000000E+00
THE ABSORBER WILL BE TREATED BY THE NORDHEIM INTEGRAL METHOD.
MASS OF MODERATOR-1 = 235.044 SIGMA(PER ABSORBER ATOM)= 1.1045741E+03
MODERATOR-1 WILL BE TREATED BY THE NORDHEIM INTEGRAL METHOD.
MASS OF MODERATOR-2 = 237.981 SIGMA(PER ABSORBER ATOM)= 7.0298355E+01
MODERATOR-2 WILL BE TREATED BY THE NORDHEIM INTEGRAL METHOD.
THIS RESONANCE MATERIAL WILL BE TREATED AS A 3-DIMENSIONAL OBJECT.
VOLUME FRACTION OF LUMP IN CELL USED TO ACCOUNT FOR SPATIAL SELF-SHIELDING=1.00000
GROUP RES ABS RES FISS RES SCAT
11 -4.204316E+00 0.000000E+00 -9.995241E+00
12 -2.380825E+01 0.000000E+00 -1.001363E+01
13 -8.898667E-03 0.000000E+00 2.751244E-02
14 -4.214681E+02 0.000000E+00 -6.774578E+01
15 -8.457773E-05 0.000000E+00 8.805284E-05
EXCESS RESONANCE INTEGRALS
RESOLVED
ABSORPTION 6.32210E+01
FISSION 0.00000E+00
PROCESS NUMBER 1007 IS AT TEMPERATURE= 293.00
Part 2: NITAWL output: Check input

## Slide 10: CSAS1X output, cont’d
GENERAL PROBLEM DATA
IGE 1/2/3 = PLANE/CYLINDER/SPHERE 3 ISN QUADRATURE ORDER 8
IZM NUMBER OF ZONES 1 ISCT ORDER OF SCATTERING 3
IM NUMBER OF SPACIAL INTERVALS 202 IEVT 0/1/2/3/4/5/6=Q/K/ALPHA/C/Z/R/H 1
IBL 0/1/2/3 = VACUUM/REFL/PER/WHITE 1 IIM INNER ITERATION MAXIMUM 20
IBR RIGHT BOUNDARY CONDITION 0 ICM OUTER ITERATION MAXIMUM 25
MXX NUMBER OF MIXTURES 1 ICLC -1/0/N--FLAT RES/SN/OPT 0
MS MIXING TABLE LENGTH 4 ITH 0/1 = FORWARD/ADJOINT 0
IGM NUMBER OF ENERGY GROUPS 27 IFLU NOT USED(ALWAYS WGTD) 0
NNG NUMBER OF NEUTRON GROUPS 27 IPRT -2/-1/0/N=MIXTURE XSEC PRINT -2
NGG NUMBER OF GAMMA GROUPS 0 ID1 0/1/2/3=NO/PRT ND/PCH N/BOTH -1
IFTG NUMBER OF FIRST THERMAL GROUP 15 IPBT -1/0/1=NONE/FINE/ALL BAL. PRT 0
SPECIAL OPTIONS
IFG 0/1 = NONE/WEIGHTING CALCULATION 1 IPN 0/1/2 DIFF. COEF. PARAM 0
IQM VOLUMETRIC SOURCES (0/N=NO/YES) 0 IDFM 0/1 = NONE/DENSITY FACTORS 38* 0
IPM BOUNDARY SOURCES (0/N=NO/YES) 0 IAZ 0/N = NONE/N ACTIVITIES BY ZONE 0
IFN 0/1/2 = INPUT 33*/34*/USE LAST 0 IAI 0/1=NONE/ACTIVITIES BY INTERVAL 0
ITMX MAXIMUM TIME (MINUTES) 0 IFCT 0/1=NO/YES UPSCATTER SCALING 0
IDT1 0/1/2/3=NO/XSECT/SRCE/FLUX--OUT 0 IPVT 0/1/2=NO/K/ALPHA PARAMETRIC SRCH 0
ISX BROAD GROUP FLUXES 0 ISEN OUTER ITERATION ACCELERATION 0
IBLN ACTIVITY DATA UNIT 0 NBND BAND REBALN PARAMETER -1
JBKL 0/1/2 BUCKLING GEOMETRY 0
WEIGHTING DATA (IFG=1)
ICON -1/0/1=CELL/ZONE/REGION WEIGHT -1 IHTF TOTAL XSECT PSN IN BRD GP TABLES 0
IGMF NUMBER OF BROAD GROUPS 27 NDSF PSN G-G OR FILE NUMBER 0
ITP 0/10/20/30/40 0/C/E/AC/A 0 NUSF TABLE LENGTH OR MAX ORDER 26
IPP -2/-1/0/N=WGTED XSECT PRINT -2 MSCM EXTRA 1-D X-SECT POSITIONS 0
IAP -1/N ANISN XSECT PRINT 0
Part 3: XSDRN-PM output: Check input and output

## Slide 11: CSAS1X output, cont’d
FLOATING POINT PARAMETERS
EPS OVERALL CONVERGENCE 1.00000E-04 DY CYL/PLA HT FOR BUCKLING 0.00000E+00
PTC POINT CONVERGENCE 1.00000E-04 DZ PLANE DEPTH FOR BUCKLING 0.00000E+00
XNF NORMALIZATION FACTOR 1.00000E+00 VSC VOID STREAMING CORRECTION 0.00000E+00
EV EIGENVALUE GUESS 0.00000E+00 PV IPVT=1/2--K/ALPHA 0.00000E+00
EVM EIGENVALUE MODIFIER 0.00000E+00 EQL EV CHANGE EPS FOR SEARCH 1.00000E-03
BF BUCKLING FACTOR=1.420892 1.42089E+00 XNPM NEW PARAM MOD FOR SEARCH 7.50000E-01
THIS CASE WILL REQUIRE 1707 LOCATIONS FOR MIXING
THIS CASE HAS BEEN ALLOCATED 100000 LOCATIONS
HW PROBLEM #1
13Q ARRAY HAS 4 ENTRIES.
14Q ARRAY HAS 4 ENTRIES.
15Q ARRAY HAS 4 ENTRIES.
DATA BLOCK 2 (MIXING TABLE, ETC.)
NUCLIDES CCCC MIXING TABLE EXTRA
ON TAPE IDENTIFICATION MIXTURE COMPONENT ATOM DENSITY XSECT ID'S
1 1092234 1 1092234 4.82827E-04
2 1092235 1 1092235 4.48073E-02
3 1092236 1 1092236 9.57449E-05
4 1092238 1 1092238 2.65827E-03
…
HW PROBLEM #1
NEUTRON GROUP PARAMETERS
GP ENERGY LETHARGY WEIGHTED BROAD GP CALC GROUP RIGHT LEFT
BOUNDARIES BOUNDARIES VELOCITIES NUMBERS TYPE BAND ALBEDO ALBEDO
1 2.00000E+07 -6.93147E-01 4.60581E+09 1 0 1
2 6.43400E+06 4.40989E-01 2.88737E+09 2 0 2
3 3.00000E+06 1.20397E+00 2.12201E+09 3 0 3
…
Part 3: XSDRN-PM output: Check input and output

## Slide 12: CSAS1X output, cont’d
HW PROBLEM #1
MIXTURE ORDER P(L) ACTIVITY TABLE QUADRATURE CONSTANTS
BY ZONE BY ZONE MATL NO. REACTION WEIGHTS DIRECTIONS REFL DIREC WT X COS
1 1 3 0 -1.00000E+00 9 0
2 5.06143E-02 -9.60290E-01 9 -4.86044E-02
3 1.11191E-01 -7.96667E-01 8 -8.85818E-02
4 1.56853E-01 -5.25532E-01 7 -8.24315E-02
5 1.81342E-01 -1.83435E-01 6 -3.32644E-02
6 1.81342E-01 1.83435E-01 5 3.32644E-02
7 1.56853E-01 5.25532E-01 4 8.24315E-02
8 1.11191E-01 7.96667E-01 3 8.85818E-02
9 5.06143E-02 9.60290E-01 2 4.86044E-02
CONSTANTS FOR P( 3) SCATTERING
ANGL SET 1 SET 2 SET 3
1 -1.00000E+00 1.00000E+00 -1.00000E+00
2 -9.60290E-01 8.83235E-01 -7.73409E-01
…
9 9.60290E-01 8.83235E-01 7.73409E-01
INT RADII MID PTS ZONE NO. AREAS VOLUMES DENS FACT RADIUS MOD SPEC(INT)
1 0 8.47431E-03 1 0 2.03935E-05 0
2 1.69486E-02 2.54995E-02 1 3.60976E-03 1.44975E-04
3 3.40503E-02 4.26791E-02 1 1.45697E-02 4.00402E-04
…
200 8.66869E+00 8.67732E+00 1 9.44315E+02 1.63291E+01
201 8.68595E+00 8.69450E+00 1 9.48079E+02 1.62454E+01
202 8.70305E+00 8.71153E+00 1 9.51816E+02 1.61635E+01
203 8.72000E+00 9.55527E+02
Part 3: XSDRN-PM output: Check input and output

## Slide 13: CSAS1X output, cont’d
OUTER INNER 1 - BALANCE EIGENVALUE 1 - SOURCE 1 - SCATTER 1 - UPSCAT SEARCH TIME
ITER ITERS RATIO RATIO RATIO PARAMETER (MIN)
1 271 -3.65574E-08 9.07818E-01 9.21823E-02 1.00000E+00 7.41645E-06 0.00000E+00 0.1135
2 432 -3.61554E-08 9.67733E-01 -6.59988E-02 -6.09758E-02 4.05880E-06 0.00000E+00 0.1740
3 585 -3.59817E-08 9.89544E-01 -2.25385E-02 -2.07275E-02 1.18926E-06 0.00000E+00 0.2325
4 714 -3.59182E-08 9.98209E-01 -8.75650E-03 -8.03183E-03 2.82780E-06 0.00000E+00 0.2828
5 840 -3.58934E-08 1.00181E+00 -3.60489E-03 -3.30243E-03 1.08569E-06 0.00000E+00 0.3305
6 944 -3.58840E-08 1.00335E+00 -1.53702E-03 -1.40816E-03 2.33462E-06 0.00000E+00 0.3708
7 1040 -3.58801E-08 1.00402E+00 -6.65941E-04 -6.08381E-04 9.85979E-07 0.00000E+00 0.4073
8 1120 -3.58780E-08 1.00430E+00 -2.87662E-04 -2.62996E-04 2.01012E-06 0.00000E+00 0.4385
9 1187 -3.58779E-08 1.00443E+00 -1.30334E-04 -1.19989E-04 8.87357E-07 0.00000E+00 0.4650
10 1254 -3.58768E-08 1.00449E+00 -5.22935E-05 -4.67008E-05 3.88977E-07 0.00000E+00 0.4917
GRP TO GRP INNER MFD MAX. FLUX MSF MAX. SCALE COARSE
ITERS INT. DIFFERENCE INT. FACTOR MESH
1 1 2 127 1.36633E-05 93 9.99998E-01 3
2 2 2 109 1.49543E-05 109 9.99998E-01 4
3 3 2 88 1.58992E-05 112 9.99999E-01 4
…
25 25 2 200 2.35314E-07 202 1.00000E+00 130
26 26 2 201 9.33659E-08 202 1.00000E+00 159
27 27 2 202 4.64712E-08 202 1.00000E+00 202
11 1304 -3.58763E-08 1.00451E+00 -2.23163E-05 -2.01096E-05 -3.25158E-06 0.00000E+00 0.5153
FINAL MONITOR
LAMBDA 1.00451E+00 PRODUCTION/ABSORPTION 2.36120E+00 ANGULAR FLUX ON 16
…
Part 3: XSDRN-PM output: Check input and output

## Slide 14: CSAS1X output, cont’d
FINE GROUP SUMMARY FOR SYSTEM
GRP. FIX SOURCE FISS SOURCE IN SCATTER SLF SCATTER OUT SCATTER ABSORPTION LEAKAGE BALANCE
1 0.00000E+00 2.10765E-02 0.00000E+00 1.74448E-02 5.80285E-03 7.23494E-03 9.61461E-03 1.00003E+00
2 0.00000E+00 1.88309E-01 6.02700E-04 1.94396E-01 6.60753E-02 4.52074E-02 7.79764E-02 9.99744E-01
3 0.00000E+00 2.14891E-01 1.37891E-02 2.42868E-01 6.80902E-02 6.42845E-02 9.62799E-02 1.00011E+00
…
26 0.00000E+00 2.07297E-12 1.28976E-13 4.19684E-14 2.72760E-15 2.19725E-12 1.97895E-15 9.99999E-01
27 0.00000E+00 4.94001E-13 3.37470E-14 5.48350E-15 5.39773E-24 5.27509E-13 2.38734E-16 1.00000E+00
28 0.00000E+00 1.00000E+00 3.06026E-01 1.82668E+00 3.06026E-01 4.27334E-01 5.74576E-01 9.99974E-01
GRP. RT BDY FLUX RT LEAKAGE LFT BDY FLUX LFT LEAKAGE N2N RATE FISS RATE FLUX*DB**2 TOTAL FLUX
1 1.48748E-05 9.61461E-03 6.76532E-05 0.00000E+00 1.57652E-03 7.18937E-03 0.00000E+00 9.39627E-02
2 1.22893E-04 7.79764E-02 5.97033E-04 0.00000E+00 2.99081E-04 4.42202E-02 0.00000E+00 8.17111E-01
3 1.53141E-04 9.62799E-02 7.71639E-04 0.00000E+00 0.00000E+00 6.19690E-02 0.00000E+00 1.04870E+00
…
26 4.09073E-18 1.97895E-15 4.61464E-17 0.00000E+00 0.00000E+00 1.87727E-12 0.00000E+00 6.14119E-14
27 4.95642E-19 2.38734E-16 5.63715E-18 0.00000E+00 0.00000E+00 4.49199E-13 0.00000E+00 7.50165E-15
28 9.24561E-04 5.74576E-01 5.01037E-03 0.00000E+00 1.87560E-03 3.83936E-01 0.00000E+00 6.70458E+00
DIRECT ACCESS UNIT 9 REQUIRES 32 BLOCKS OF LENGTH 896 FOR CROSS SECTION WEIGHTING.
Part 3: XSDRN-PM output: Check input and output

## Slide 15: Parametric studies #1-#3
PS#1: Play with homogeneous water/U-235 to find the optimum H/U ratio
PS#2: Increase the radius of a U-235 sphere to see effect on k-effective
PS#3: Increase the radius of water surrounding a 6.5 cm radius U-235 sphere

## Slide 16: PS#1: Homog. H/U

## Slide 17: PS#2: Adding more U235 (to 6.5 cm radius U235 Sphere)

## Slide 18: PS#3: Adding water reflect’r (to 6.5 cm radius U235 Sphere)

## Slide 19: PS#4: Mixing water into U235 (fixed size sphere)

## Slide 20: PS#5: Mixing water to sphere (fixed U content = water balloon)

## Slide 21: PS#6: Test of Reflectors
Base = 5 cm radius U235
  Absorption = 41.3%
  Leakage = 114.3%
  Resulting k-effective = 0.641
Test k-effective from adding reflector:
  Water
  Boron
  SS304
  Pb
  U-238
Put them in order

## Slide 22: PS#7: Effect of gaps
Base = 6.36 cm radius U235 with “infinite” water reflection
Vary the gap between the U235 and the water to find effect on k-effective

## Slide 23: PS#7: Adding void gap (to reflected 6.36 cm U235 Sphere)

## Slide 24
SCALE Sequence CSAS25

## Slide 25: New SCALE features
Use of INFHOMMEDIUM
  MULTIREGION used before to turn XSDRNPM on
  INFHOMMEDIUM indicates that our assumption is that the resonance materials appear in large chunks: What we will do for CSAS25
Use of KENO geometry

## Slide 26: CSAS25 input: KENO geometry
Limited three dimensional description
  No intersection of surfaces
  Arranged in “Units”: See manual C4
  Units built from the inside out
  “Holes” allow for inclusion of units into the overall geometry
Two examples:
  Tokaimura accident
  Parametric study

## Slide 27: Fig. 2-2 results

## Slide 28: CTS Tokai input
URANYL NITRATE SOURCE
27GROUPNDF4 INFHOMMEDIUM
SOLNUO2(NO3)2 1 370 1.00 1.0 293 92235 18.8 92238 81.2 END
H2O 2 1 END
ss304 3 1 END
END COMP
URANYL NITRATE SOURCE
READ PARM GEN=203 NPG=500 RUN=YES PLT=YES END PARM
READ GEOM
GLOBAL UNIT 1
Cylinder 1 1 25.0 +12.25 -12.25
Cylinder 3 1 25.3 +12.55 -12.55
cylinder 2 1 27.8 +12.55 -12.55
END GEOM
READ BOUNDS ALL=VOID END BOUNDS
END DATA

## Slide 30: CSAS25: Where is the answer?
Search on “best”
Gives you the k-effective with uncertainty

## Slide 31: More complicated KENO example

## Slide 32: Discussion of Experiments
Critical “Benchmarks”: Tie codes to reality
Static criticality experiments
  Direct application - Requires good fit to your situation
  Criticality curves - Typical configurations and materials
  Validation of computer codes: Finding area of applicability
    Interpolation
    “Bracketing”
Dynamic criticality experiments
  Fission yields
  What stops the accident?
    Temperature (metals)
    Boiling
    Material ejection
    Human reaction (very slow)

## Slide 33: Important Considerations for Benchmarks
Well defined compositions
Precise dimensions
Regular geometries (for modeling)
  Requires some isolation from “rest of the world” = piping, tables, floors, etc.

## Slide 34: Nature of Experiments
Critical dimensions
  Height of solutions
  Radius of spheres
  Thickness of slabs
Critical spacing of arrays
Various material effects
  Reflection
  Poisons
  Moderators
Inverse multiplication
  Approach to critical

## Slide 35: Subcritical in-situ Experiments
Best of all = Test the actual materials, geometry, environment (ANSI/ANS 8.6)
Hard to model all accident conditions
  Chernobyl was an in-situ experiment

## Slide 36: Objectives
Overview of
International
Handbook of
Evaluated
Criticality
Safety
Benchmark
Experiments

## Slide 37: What?
Collection of EVALUATED benchmark critical, subcritical, and (some) alarm placement experiments
  Someone did and published the experiment (You hope!)
  Someone else (you?) writes it up and submits to the Benchmark Book
  Reviewed
  Included in next revision of BB
Suitable for reproduction to validate computer code
All sorts of fissile materials, absorbers, geometries, interactions, etc.

## Slide 38: Who?
Sponsored by OECD-NEA
Put together by Dr. Blair Briggs of INEL
Hundreds of participants world-wide from multiple countries

## Slide 39: Why?
The purposes of the International Criticality Safety Benchmark Evaluation Project (ICSBEP) Working Group are:
Identify and evaluate a comprehensive set of benchmark critical and subcritical experiment data;
Verify the data, to the extent possible, by reviewing original and subsequently revised documentation and by talking with experimenters or individuals who were associated with the experiments or the experimental facility;
Evaluate the data and quantify overall uncertainties through various types of sensitivity analyses;
Compile the data into a standardized format;
Perform sample calculations of each experiment with standardized criticality safety neutronics codes; and
Formally document the work into a single source of verified and extensively peer reviewed benchmark critical data.

## Slide 40: Get it on your computer
Not a controlled document
Can be freely distributed
415 experiments
I recommend that you Google it and sign up (not required for this course, but it doesn’t matter)

## Slide 41: Benchmark book sections
From “Study and Perspectives of the OECD/NEA Working Party on Nuclear Criticality Safety Projects,” M.C. Brady-Rapp, et al., 1999.

## Slide 42: Benchmark book sections (2)
From “Study and Perspectives of the OECD/NEA Working Party on Nuclear Criticality Safety Projects,” M.C. Brady-Rapp, et al., 1999.