## Slide 1: Lectures 6&7: Variance Reduction Techniques
Mathematical basis
Simple two-choice example of power of biasing to reduce variance
Fundamental variance reduction techniques
  Absorption wt’ing
  Splitting
  Forced collision
  Russian roulette
Exponential transform
Source biasing
Cell wt’ing
Weight windows
DXTRAN spheres

## Slide 2: Rules of “Biasing”
Choosing from a probability distribution that WE want to use rather than natural
Particle weight = Parts of particles
Basis: If natural is , but we want to use we have to apply a weight correction of:
(In general) All possible x's in the original distribution are still possible in the new distribution.

## Slide 3: Example: Using Flat Distributions
It is entirely unbiased (i.e., okay) for you to choose an x uniformly and adjust the weight contribution weight by multiplying the previous weight by the correction:
Unfortunately, although it is unbiased to do this, it is also usually unwise.

## Slide 4: Why Do It?
We do it to make our Monte Carlo programs better. "Better" means "lower variance."
Lower variance, in view of our "black box" view of Monte Carlo:
means "have the x's come out as nearly identical as possible."

## Slide 5: Simple Example
As the simplest possible example, find the optimum biasing probabilities for the following 2-choice situation:
i |  | I |  | wcorr | I | Error | Error2
1 | .2 | 6 |  |  |  |  | 
2 | .8 | 1 |  |  |  |  | 

## Slide 6: Our slab example
As the simplest possible example, find the optimum biasing probabilities for the following 2-choice situation (Choice of original group):
i |  | I |  | wcorr | I | Error | Error2
1 | .4 | 0.000734 (s=0.027) |  |  |  |  | 
2 | .6 | 0.000026 (s=0.005) |  |  |  |  | 

## Slide 7: Common Variance Reduction Techniques
Non-physical distributions that have been proven useful
For each of them, we will use same pattern:
  General description ("heuristics") of what the idea is.
  Which of the transport decisions is being adjusted and what the physical distribution is.
    Particle initial position
    Particle initial direction
    Particle initial energy
    Distance to next collision.
    Type of collision
    Outcome of a scattering event
  Non-physical distribution that we will use.
  Resulting weight correction.

## Slide 8: Absorption Weighting
“Weighting in lieu of absorption”
This is the most commonly used variance reduction technique. In fact, in many transport codes, this option cannot be turned off.
General description: The basis idea is to PREVENT particles from absorbing. Then particles will live longer and have more of a chance to score.
Which of the transport decisions is being adjusted?
  #5. Type of collision.

## Slide 9: Absorption Weighting (2)
Mathematical layout: Assume the two possible outcomes are scattering and absorption. The natural p.d.f.'s are:
  Scattering with probability
  Absorbing with probability
  Our decision is to pick scattering with a 100% probability.
Resulting weight correction:

## Slide 10: Absorption Weighting (3)
Note that we have made a POSSIBLE choice (absorption) IMPOSSIBLE. This is allowed ONLY because absorbed particles have NO possibility of contributing to the answer.
In addition to a lower variance (per history), we are ALSO guaranteed to have higher computer run times, since each history will be longer.
May or may not be worth it.
Another way of looking at this: Divide particle into two parts: the fraction that scatters and the fraction that absorbs. We continue to follow only the first (scattering) and let the fraction that absorbs die.

## Slide 11: Splitting
Forms the basis for other variance reduction techniques.
Does not really fit the pattern of MODIFYING the probability distribution.
Instead, the single particle becomes multiple particles

## Slide 12: Splitting (2)
Two common situations in particle transport that involve splitting:
  Particles emitted from a collision, one of them is followed as a continuation of the current particle history, and then, after the original particle history is over, we come back and "pick up" the second particle from the original collision site and follow IT to conclusion.
  Particle is split into two or more "pieces" when an "important" region is entered in order to even out the statistics.
Basic mathematical idea of splitting is that ALL of the options of a discrete probability distribution are followed with weight corrections proportional to the discrete probabilities.

## Slide 13: Splitting (3)
Example: Assume that a history (in progress) with weight of 0.5 faces a discrete decision with three possible outcomes:
  State 1 with a 60% probability;
  State 2 with a 30% probability; and
  State 3 with a 10% probability.
Instead of choosing between the three, we follow each of them in turn.
  Continue the history by following the history into State 1 with a weight of 0.30 and "bank" (i.e., save in a special file of "states" to be continued later) one history in State 2 with weight 0.15 (=30% of 0.5) and one history in State 3 with weight 0.05.
After a particle history ends, we return to banked particles until the bank is empty.

## Slide 14: Forced Collisions
General description: FORCE a collision in a particular section of the path of a particle. We will use it in a particular way, not allowing particle to escape.
Keeps particles alive longer, so should increase contribution to all scores
Which of the transport decisions is being adjusted: #4. Distance to next collision.

## Slide 15: Forced Collisions (2)
Mathematical layout: This is a splitting technique: the particle is divided between the part that DOES collide in the desired region and the part the DOES NOT collide in the desired region.
Assume the distance to the boundary is t0 (in mean free paths)
Actual probability distribution:
  Probability of escaping:
  Non-escape with probability:
Our decision non-escape with probability 1.00.

## Slide 16: Forced Collisions (3)
Weight correction:
Remember the splitting "roots" of this procedure, and recognize that the "other " part of the particle DOES escape. Therefore, we should contribute
to the leakage of the closest boundary, where w is the weight BEFORE the correction.
Again, possible that longer computer run time will hurt more than lower variance will help.
  In fact, most of the literature indicates that this is USUALLY that case, so that "non-escape" forced collision is seldom used.

## Slide 17: Russian Roulette
Like splitting, mathematical tool that is needed for implementing variance reduction techniques.
Idea: COMBINE several particles into one particle by selective killing.
Mathematics: Have a particle DIE with a high probability of 1-p (typically 90-99%).
To keep the method unbiased, if a particle survives, its weight is increased by a factor of 1/p.

## Slide 18: Russian Roulette (2)
Need for this tool is obvious when used in combination with absorption weighting and forced collision--the latter two methods eliminate BOTH ways of ending a history. Without the (artificial) death condition added by Russian Roulette, the first history would never end!
In practice, Russian Roulette is performed whenever a particle's weight falls below a lower weight cutoff,
  Although not formally reducing the variance, it increases the efficiency of a Monte Carlo process by saving the computer time that would otherwise be wasted following low weight particles.

## Slide 19: Exponential Transform
General description: The basis idea of the exponential transform technique is to make it EASIER for a particle to travel in a desired direction by THINNING the material in the desired direction and making the material DENSER in directions away from the desired direction.
  Does NOT make it more LIKELY that desired directions will be chosen, just easier to travel in desired directions.
Which of the transport decisions is being adjusted?
  #4. Distance to next collision.

## Slide 20: Exponential Transform (2)
Mathematical layout: Change the total cross section and make it dependent on the direction traveled. Denoting the cross section used with an asterisk, we have:
where p is a general parameter chosen by the user (or programmer) with 0<p<1 and is the desired direction.
Because of the limitations on p (0<p<1) these minimum and maximum values range from 0 to twice the true cross section.

## Slide 21: Exponential Transform (3)
The exponential transform just involves modifying the cross sections used in translating mean free paths to centimeters.
Two cases that have to be considered: The particle reaches the outer boundary or it collides inside the problem geometry.
Actual probability distribution:
  Probability of escaping:
  Probability of next collision at distance s:

## Slide 22: Exponential Transform (4)
For each of these two conditions, the probability distributions actually used are:
  Probability of escaping:
  Probability of next collision at distance s:
Resulting weight correction:
  If the particle escaped:
  If the particle collided at distance s:

## Slide 23: Source Biasing
General Description: The most general of the variance reduction techniques. The basic idea is simple: Instead of using the true distribution, use some other distribution, i.e., that you have some reason to believe is better.
Which of the transport decisions is being adjusted?
  #1-#3. Initial source position, energy, and direction.

## Slide 24: Source Biasing (2)
Mathematical layout and weight correction:
In the basic layout of the idea, no guidance is actually given about distributions to use. Therefore, all we have is the basic theory laid out above in the "Mathematical basis of cheating" section:
  "So, if the probability distribution dictated by the physics is and we want to use a second distribution , we can do it if we use a weight correction,

## Slide 25: Choosing Modified Distribution
In general, you want to modify the natural distributions in order to favor choices that are more IMPORTANT.
What is "importance"? To us the answer is simple:
IMPORTANCE = EXPECTED CONTRIBUTION
Therefore, our job is to modify the distributions to favor following the particles that are the expected to contribute the most to the "score“.

## Slide 26: Choosing Modified Distribution (2)
How much should we favor these choices?
If you know the importance of each of your possible choices, I(x), the theoretically optimum choice of your alternate distribution is given by:
The successful approaches I have seen to picking alternate distributions fall into the following three categories:
  Heuristic (i.e., seat of the pants) choices,
  Choices based on preliminary MC calculations, and
  Choices based on preliminary non-MC calculations.

## Slide 27: Category 1: Heuristic
Modify the natural distribution to favor the choice of particles that you think MUST BE more important.
  EXAMPLE 1: Source particle location (Decision #1) If you are interested in determining the right leakage, pick source locations preferentially to the right
  EXAMPLE 2: Source direction (Decision #2) If you are interested in determining the left leakage, pick source directions preferentially heading to the left.
  EXAMPLE 3: Source energy (Decision #3) If you are interested in deep penetration, pick source energies where total cross section is low.
You are left to your own intuition about HOW MUCH to favor the more important particles. Therefore, this approach is trial and error.

## Slide 28: Category 2: Preliminary MC Calculations
This technique is based on you running a few (hopefully) short "test runs" to get the relative importance of various initial source choices.
The test cases correspond to restricting the choices of one of the variables to a sub-domain, running a short problem, and interpreting the resulting answer as the importance of the sub-domain and using:
There is an automatic Weight Windows Generator in MCNP that does this for you: Generates data during ONE run to collect data to speed up the NEXT run.
  We will be using this tool in a later tutorial

## Slide 29: Category 3: Preliminary Non-MC Calculations
As we will study later in the course, we can actually write and solve an equation for the importance function for source particle (and scattered particle) distributions.
This equation can be approximately solved using deterministic methods (e.g., discrete ordinates) for the importance function, which can then be used in the MC calc
We will postpone this state-of-the-art topic to explore in more detail later

## Slide 30: Cell Weighting in MCNP (And Beyond)
Rules:
When you pass from “region” of lower weight to higher weight, split by ratio
When you pass from HIGHER to LOWER, play Russian Roulette with survival probability of

## Slide 31: Weight Windows in MCNP
Rules:
When you pass from OLD to NEW, adjust weight to stay in a desired window of weights for each cell:
  Use RR and splitting as before, utilizing

## Slide 32: Importance Mesh Grids
Latest variance reduction technique in MCNP
Overlay the REAL problem geometry with a regular Cartesian grid of cells with importance function given
  Regularizes the spatial density of importance function
  Importance functions can be found from a deterministic calculation
Corresponding mesh tallies available as well (in MCNP)

## Slide 33: DXTRAN Spheres
MCNP-specific VR method
Put a sphere in the problem somewhere and split EACH emerging particle (including source) into 2 parts: a part that passes through the sphere and a part that doesn’t
Typical splitting strategy with one exception: Very difficult to determine the “theoretical” weight of each particle (which is based on the total probability of hitting the sphere)

## Slide 34: DXTRAN Spheres (2)
Clever solution to problem: Stochastically determine the probability:
  Choose ONE direction that is headed toward the sphere (with weight correction)
  Translate the “DXTRAN” particle to the surface of the sphere (with weight correction)
  Make NO correction to the weight of the OTHER particle (that does not go directly to the sphere)
    BUT kill the particle if it touches the sphere on the next flight

## Slide 35: FOM
  Figure of Merit (FOM) is a method of comparing MC runs for efficiency:
  Based on:
      and the assumption that N~T,
      the FOM should be approximately constant.

## Slide 36: FOM (2)
  Printed out by MCNP in a table at the end (at ~10 times during the run), it can be used several ways:
    To compare different computer systems
    To check the efficiency gains (?) from a variance reduction technique
    To check that the problem is proceeding “smoothly”

## Slide 37: FOM (3)
  FOM table (on one tally only) and finish
  …
  tally 11
  nps mean error vov slope fom
  1000 1.5133E-02 0.2017 0.0564 0.0 788
  2000 1.3912E-02 0.1496 0.0311 0.0 723
  3000 1.4250E-02 0.1187 0.0198 0.0 773
  4000 1.4203E-02 0.1044 0.0154 0.0 747
  5000 1.5107E-02 0.0911 0.0114 0.0 788
  6000 1.3896E-02 0.0860 0.0103 0.0 740
  7000 1.4112E-02 0.0787 0.0087 0.0 758
  8000 1.4461E-02 0.0726 0.0073 0.0 778
  8546 1.4406E-02 0.0701 0.0068 0.0 780
  ***********************************************************************************************************************
  dump no. 2 on file tut1r nps = 8546 coll = 1106205 ctm = 0.26 nrn = 15526679
  3 warning messages so far.
  run terminated when it had used 0.2 minutes of computer time.
  computer time = 0.36 minutes