## Slide 1: Lesson 5 Objectives
Finishing up Chapter 1
Development of adjoint B.E.
  Mathematical elements of adjoints
  Application to the terms of the B.E.
  Use of adjoint in source/detector problems

## Slide 3: Uses of adjoint
Uses of the adjoint in shielding applications:
  Alternative way of performing shielding problems
  Efficient way to partition a complex problem
  Way to convert a physical detector (e.g., person) into an “equivalent” response function
  As a graphical tool for illustrating the important particle paths in a shielding analysis (i.e., the product y*y is Mark Williams’ “contributon” flux, the distribution of particles that are “destined” to be detected).
  Importance function for emerging particles in a Monte Carlo calculation (NE582)
  Basis of perturbation methods

## Slide 4: Mathematical terms we will use
“Function”=converts scalar to another scalar
“Functional”=converts function to scalar
“Operator”=converts function to another function
Inner product (cf. Bra-ket) notation=simple(r) notation for integration. For us:
Definition of L*, the operator adjoint to L:

## Slide 5: Our operator
Becomes for us:

## Slide 6: Our operator (2)
where:
We are going to find the operator L* that is adjoint to L.
  Why would we want to do this?

## Slide 7: Why? Why? Why?
We can get a detector response two ways:

## Slide 8: Use of Adjoint in Source/Detector
There are several uses of adjoint B.E.
We will examine it in a Source/Detector problem:
Source
Detector
Volume V
Surface S

## Slide 9: Traditional Forward Solution
In the typical forward solution, one uses a computer code to solve operator relation:
in Volume V
Once is known, we “fold” the flux into the detector response function to get the detector response, R, using functional:

## Slide 10: Equivalent Adjoint Analysis
Alternatively, the analyst can use a computer code (usually the same one) to solve:
in Volume V
Once is known, we “fold” the adjoint flux into the SOURCE distribution to get the SAME detector response, R:

## Slide 11: A little more abstract
A FORWARD calculation involves DEDUCING the consequences of the presence of a SOURCE. It results in a particle flux distribution that can be used to make a DOSE MAP.
On the other hand, an ADJOINT calculation involves deducing the consequences of the placement of a DETECTOR. It results in a adjoint flux distribution that can be translated into a DETECTOR SENSITIVITY MAP. (i.e., a map of what source locations a detector can “see”).

## Slide 12: Adjoint or forward?
Q: If either way gives the same answer, how do you choose between the forward and adjoint modes?
A: Both methods involve two steps:
  Solve for forward or adjoint flux (expensive)
  Integrate flux over response function or source (cheap)
Therefore, you should choose the mode that minimizes expense:
  FORWARD if you have 1 source, many detectors
  ADJOINT if you have 1 detector, many sources

## Slide 13: Development of Adjoint B.E.
We will be developing the Adjoint form of the Boltzmann Equation with the following steps:
  Mathematical elements of adjoints
    Introduction of special notation
    Discussion of WHAT an adjoint operator is
  Application to the terms of the B.E.
    Use of a “cookbook” approach to (tediously) translate each term of the B.E. into adjoint
  Physical derivation of adjoint
    WHAT the adjoint flux means
  Use of adjoint in source/detector problems

## Slide 14: Special mathematical notation
Operator notation:

## Slide 15: Special mathematical notation (2)
Inner product (cf. Bra-ket) notation:
Definition of L*, the operator adjoint to L:
We will use this definition both to convert each of the four “sub-terms” of the B.E. into the adjoint form and to demonstrate the usefulness of the adjoint B.E.

## Slide 16: Converting to adjoint form
Our conversion of the four subterms will follow the following procedure:
Form the “left-hand-side” for the sub-term:
Reverse the positions of a and b inside the resulting equation.
Rearrange (if necessary) the integrals into the form:
Isolate the new operator term,

## Slide 17: Interaction term, L2
Form the “left-hand-side” for the sub-term:
Reverse the positions of a and b inside the resulting equation.
Rearranging (if necessary) the integrals into the form:
Isolate the new operator term,

## Slide 18: Interaction term, L2 (2)
Rearranging (if necessary) the integrals into the form:
Isolate the new operator term:
with:
So, the first term is so-called “self-adjoint”

## Slide 19: Scattering term, L3
Form the “left-hand-side” for the sub-term:
Reversing the positions of a and b inside the resulting equation (after moving a inside)

## Slide 20: Scattering term, L3 (2)
Rearranging the integrals into the form:
Exchange primed and unprimed:

## Slide 21: Scattering term, L3 (3)
Isolate the new operator term:
Note that the energy direction of scatter has been reversed

## Slide 22: Fission term, L4
Form the “left-hand-side” for the sub-term
Reversing the positions of a and b:

## Slide 23: Fission term (2)
Rearranging the integrals into the form:
Exchange primed and unprimed:

## Slide 24: Fission term (3)
Isolate the new operator term:
Note the interesting swap of the roles of the cross sections and chi function.

## Slide 25: Leakage term, L1
Form the “left-hand-side” for the sub-term:
Reversing the positions of a and b inside the resulting equation.
  This is more difficult because of the divergence operator
  We must use the vector product rule:

## Slide 26: Leakage term, L1 (2)
  Rearranging this to:
  Substituting this gives us

## Slide 27: Leakage term, L1 (3)
Isolate the new operator term
  We are only partially successful.
  The operator can be identified as:
  but only if we can guarantee that:
If we cannot set this term to 0, then it will have to be dealt with in some way.

## Slide 28: Final form of the Adjoint B.E.
Putting the terms together, we get:

## Slide 29: Solution of the Adjoint Equation using a “Forward” code
Although we have not yet studied how the forward equation is solved in modern computer codes, let us assume that such codes can written.
A term-by-term comparison of the forward and adjoint operators indicates that we can “fool” a forward code into solving the adjoint problem with a little data manipulation:
  Reversing the scattering cross sections: Make upscatter into downscatter and vice versa
  Reverse the roles of
  Interpret directions backwards: adjoint fluxes are turned around 180 degrees
  Reverse the roles of the source and response function
Steps 1 & 2 are cross section manipulations, implemented i practice by having “forward” and “adjoint” cross section libraries
Steps 3 & 4 are left to the user to implement in the problem setup and answer interpretation

## Slide 30: A little legalism
Remember that we REALLY came up short in our development of the adjoint, arriving at:
If you remember (or even if you don’t), we have a divergence theorem that tells us:

## Slide 31: A little legalism (2)
Therefore the “troublesome” term can be written as a surface integral:
And a careful examination of the boundary conditions of the forward and adjoint problems will convince you that this term must be 0 (y=0 on the surface for INCOMING directions, y*=0 for OUTGOING directions)

## Slide 32: Adjoints and boundary sources
An important class of shielding problems do not fit the source/detector geometry we have been using, but instead involve boundary fluxes serving as sources:
Detector
Volume V
Surface S
Boundary flux
as a surface
source

## Slide 33: Adjoints/boundary sources (2)
For this situation, the derivation becomes a little different and involves the SURFACE term that we previously eliminated:

## Slide 34: Adjoints/boundary sources (3)
The resulting choice that the analyst has is to either solve:
and use the flux to get the detector response the “normal” way:
OR

## Slide 35: Adjoints/boundary sources (4)
Solve the “normal” adjoint problem:
and use the adjoint flux and boundary fluxes to get the detector response using:
The adjoint path is especially useful in “do-it-yourself” response function creation: Run an adjoint on a “detector” object you define (e.g., human phantom, battle tank) and then subsequently use the surface adjoint flux as a response function for the object.

## Slide 36: Surface scoring
This “surface source” methodology can even be applied to “normal” source/detector problems by partitioning the problem into a “source side” (V1) and a “detector side” (V2) :
Source
Detector
Volume V2
Surface S
Volume V1
Partitioning surface PS

## Slide 37: Surface scoring (2)
The detector response is given by the surface integral:
where the integral need only be taken over the Partitioning Surface PS because (like before) the external boundary conditions guarantee that the product y*y is 0 on all external surfaces.
Note that the partitioning surface can be ANY surface that completely separates the source and detector