## Slide 1: Lesson 7 Objectives
Definition of “outer” (energy) iteration
Reduction to one-group analysis: Stand-in for space-direction calculations
Expected convergence rate
Simple algorithm
Solution of sample problem in infinite medium

## Slide 2: Energy solution strategies: Fixed source
The resulting energy group equations are coupled through scattering and fission
We will first deal with non-fission situation, where the group equation is:

## Slide 3: “Outer” iteration solution strategies (1)
There are two iterative approaches that are in common use Jacobi and Gauss-Seidel.
  We will use to count iterations (where
  means an original guess of the fluxes)
Jacobi (“simultaneous update”) uses:
Key point = the scattering source comes from flux of the previous generation

## Slide 4: “Outer” iteration solution strategies (2)
Gauss-Seidel (“successive update”) uses:
Key point = for groups that have already been calculated in the CURRENT outer iteration, you use the NEW fluxes when calculating the down-scattering source term.

## Slide 5: “Outer” iteration solution strategies (3)
In practice, the groups are solved one at a time (group 1, then group 2, etc.) A single sweep through all groups is called an OUTER ITERATION.
  We continue iterations, sweeping through all groups over and over, until the absolute value of the fractional change in ANY group flux value is less than a given “convergence criterion” (user-defined).
The G-S approach takes advantage of the fact that, for groups of LOWER number, the current iteration has already been done.
For many problems (esp. photon and “fast” group structures) one outer iteration is all that is required (no up-scatter)
Bottom Line: We can worry about space and direction for ONE group at a time

## Slide 6: Infinite medium: Fixed source
For the idealized problem of an INFINITE uniform medium, the group fluxes do not depend on either flux or direction (so each direction flux is the same as the scalar flux):
So, the group balance equations (excluding fission) are:
or (Removal formulation)

## Slide 7: Analysis of 1-group eqn.
Basic idea: We can attack the B.E. as a series of ONE GROUP problems in space and direction
  The effects of other groups will be BURIED in the scattering-in source term
Therefore, each group’s solution for spatial/direction flux will use methods (e.g., FORTRAN subroutines) that IGNORE energy
  This is of enormous value in MODULARIZING the computer codes

## Slide 8: 1-group analysis (2)
The equation for group g is:
where:
NOTE: The scattering that stays inside the group is still in the first equation.

## Slide 9: 1-group analysis (4)
With the group g flux on the right side AND the left side, we proceed by introducing ANOTHER LEVEL of iteration, the INNER iteration:
where k is the inner iteration counter.
This inner iteration has an interesting physical interpretation. If you set the initial flux (which is traditionally referred to “Iteration Zero”) to zero:
then

## Slide 10: Expected inner convergence rate
This physical analogy leads us to expect that the convergence rate of the inner iterations (i.e., how quickly we expect the flux to settle down) will depend on how important within-group scattering is:
Therefore:
  High absorption problems=fast convergence
  High scattering, low absorption=slow convergence
REMEMBER: We are inside a group, so the scattering term is the “within-group” scattering.

## Slide 11: “Inner” iteration solution procedure
Set initial flux guess to zero in each group
For each energy group (high to low):
  Find Sg using fixed source and other group fluxes
  Using latest group flux, add within-group scattering source to RHS to Sg
  Solve for new group flux [REST OF COURSE]
  Repeat steps B&C to “inner” convergence of flux
Repeat step 2 to “outer” convergence of flux.
Be sure NOT to reset the fluxes to zero (i.e., do NOT return to step 1!). Start with the best fluxes you have for each group.

## Slide 12: Summary: Infinite medium procedure (with INNER iterations)
For infinite-medium problems, the group equation simplifies to:
With procedure:
Set initial flux guess to zero in each group
For each energy group (high to low):
  Find Sg using fixed source and other group fluxes
  Using latest group g flux, add within-group scattering source to RHS
  Solve for new group g flux using first equation above
  Repeat steps B&C to “inner” convergence of flux
Repeat step 2 to “outer” convergence of flux.

## Slide 13: Summary: Infinite medium procedure (removal formulation)
For infinite-medium problems, the group equation simplifies to:
With procedure:
Set initial flux guess to zero in each group
For each energy group (high to low):
  Find Sg using fixed source and other group fluxes
  Solve for new group g flux using first equation above
Repeat step 2 to “outer” convergence of flux.
NOTE: This only works for infinite medium calculations.

## Slide 14: Homework 7-1
Group
1 2 3
Total 0.6 0.8 1.0
Scat to 1 0.4 0.1 0.1
Scat to 2 0.1 0.3 0.1
Scat to 3 0.05 0.3 0.4
Source 1 0 0
Write the balance equations for each group using the removal formulation
Solve for the group fluxes (without INNER iterations) using:
  Jacobi numerical scheme (convergence of 1.e-6)
  Gauss-Siedel numerical scheme (convergence of 1.e-6)
Collapse to 1 group total, source, scattering, absorption cross sections, solve for the flux, and verify that it is equal to the sum of the original 3 group fluxes.

## Slide 15: Homework 7-2
Group
1 2 3
Total 0.6 0.8 1.0
Scat to 1 0.4 0 0
Scat to 2 0.1 0.3 0
Scat to 3 0.0 0.3 0.4
Source 1 0 0
Write the group balance equations using full formulation (with INNER iterations)
Solve for the group fluxes (using INNER iterations), one group at a time with Gauss-Siedel. Use a 1.e-6 convergence criterion for the inner iterations. (One outer iteration is all you need.)
Collapse to 1 group total, source, scattering, absorption cross sections, solve for the flux, and verify that it is equal to the sum of the original 3 group fluxes.